## Slide 1: Robotic Simulator Controller

## Slide 2: Overview
V-REP, scenes, scripts and controlling objects remotely
   Tobias Bauer
Development problem and Server adapter solution
     Pongwanit Jeaperapong
App and hardware
 Rui Choo

## Slide 3: The Scene
IRB_140 Robot
Gripper
Vision Sensor
Blocks
Conveyor belts
Conveyor belt sensors

## Slide 4: The Task

## Slide 5: Simulation scripts
Written in LUA
Attached to models
Non-threaded/threaded child scripts
recommended to use non-threaded:
initialisation
actuation
sensing
restoration

## Slide 6: Controlling the robot
IRB 140 child script (pseudo code)
Initialisation -------------------------
signal move = 0
-----------------------------------------
Actutation ---------------------------
If signal “move“ != 0
rotate(signal move)
-----------------------------------------
function rotate (velocity)----------
jointOrientation += velocity
-----------------------------------------
Java Program
Set signal

## Slide 7: Introducing V-REP Remote API
Want to develop application that interface with V-REP ?
Remote API library is available in
C++, Python, Java, Matlab, Octave, Lua, Urbi
Source code available for self compiling
Doucmentation available in V-REP website
http://www.coppeliarobotics.com/helpFiles/en/apiFunctions.htm

## Slide 8: libremoteApiJava native library problem
.dll for Windows
.so for Linux
.dylib for macOS
All for x86-64 CPU architecture
libremoteApiJava.so provided do not run on Android ARM
“java.lang.UnsatisfiedLinkError”

## Slide 9: Trying to recompile for ARM
Installing arm-linux-gnueabi-g++
Editing makefile
  Change from gcc++ to arm-linux-gnueabi-g++ and
  Change include directory from OpenJDK to Android NDK ARM
  Original Modified

## Slide 10: Trying to recompile for ARM
“java.lang.UnsatisfiedLinkError: dlopen failed: library "libpthread.so.0" not found”
extApiPlatform.c line 50: #include <pthread.h>
Android has no libpthread.so.0
Desktop Linux has libpthread.so.0

## Slide 11: Server Adapter Solution
1.Send custom command
2.Translate command to V-REP API call
3.Send V-REP API call
4.Robot moves
5.Send related data
6.Forward related data

## Slide 12: Example of Translation
“SIMULATION\n1\n” -> vrep.simxStartSimulation
“SIMULATION\n2\n” -> vrep.simxPauseSimulation
“MOVEMENTDATA\n*number*\n*number*\n” ->
vrep.simxSetFloatSignal(…,”rotate”,…) and vrep.simxSetFloatSignal(…,” moveUpDown”,…)
“MOVEMENTDATAVIABUTTON\n*string* \n” ->
vrep.simxSetFloatSignal(…,”rotate”,…) or vrep.simxSetFloatSignal(…,” moveUpDown”,…)
“GRIPPERDATA\n*number*\n” ->
vrep.simxSetFloatSignal(…,” closeGripper”,…)

## Slide 15: Android Sensors
Accelerometer
Gyroscope
Rotation Vector

## Slide 16: Android Sensors
Available in virtually all devices
Accelerometer
Uses much less battery than the gyroscope

## Slide 20: What is V-REP?
Robot simulator with IDE
Objects controlled via embedded script over
      plugin
      ROS node
      custom solution
      remote API client
  Controllers can be written in
      C/C++
      Python
      Matlab
      Octave
      Java
      Lua

## Slide 21: Thank you for your attention